## Slide 1: Simplex Control and Message/ACK Exchange - Module 6 Final Presentation
Le Wang: lewang@wpi.edu
Renato Iida: rfiida@wpi.edu
Rebecca Cooper: rrcooper@wpi.edu

## Slide 2: Outline
Purpose
Data Transmission in the MAC Layer
Implementation
Interfacing with the other Modules
‘End-to-End’ Simulation of Data Transmission and ACK Response
Lessons Learned

## Slide 3: Purpose
Establishing end-to-end network resource allocation management in simplex mode.
Exchanging of control information and message/ACK forwarding between the UEs and the BS units.

## Slide 4: Data Transmission in the MAC layer
The Evolution of the MAC Frame
State Machine for the Frame Transmission
ACK Timeout
Other Features Considered

## Slide 5: Building the MAC Frame
The package format must be small enough that it is easy to handle
It must also convey useful information
  Receiver UE
  Sender UE
  Data
Receiver UE
1 byte
Sender UE
1 byte
Data

## Slide 6: Building the MAC Frame
Receiver UE
1 byte
Sender UE
1 byte
Data
Option 1
Routing Path
1 bytes
Option 1
Receiver Base Station
1 byte
Sender Base Station
1 byte
The Routing between Base Stations:
Transmit the entire routing path
  This is very long
  It requires additional processing at the Base Station

## Slide 7: Building the MAC Frame
Receiver UE
1 byte
Sender UE
1 byte
Data
Option 2
Routing Path
1 bytes
The Routing between Base Stations:
Transmit the next stage in the path
  The Base Station must change the value of this field every time

## Slide 8: Building the MAC Frame
Receiver UE
1 byte
Sender UE
1 byte
Data
Option 3
Base Station
Read the receiver and sender at the Base Station and determine the routing
  Easy to understand
  The header stays small
The Routing between Base Stations:

## Slide 9: Building the MAC Frame
Frame Type
1 byte
Differentiates between the uses of the MAC frames
The INVALID frame type is used to drop corrupt frames
Also helps with error detection through hamming distance
  DATA 1111 0000 = 240
  ACK 1111 1111 = 255
  INVALID 0000 0000 = 0
Receiver UE
1 byte
Sender UE
1 byte
Data
(optional)
Frame Type:

## Slide 10: Building the MAC Frame
Data Size
1 byte
Set a maximum size for all MAC frames of 240 bytes or 1920 bits
Transmitting the data size allows us to cut off padding added by the physical layers
Frame Type
1 byte
Receiver UE
1 byte
Sender UE
1 byte
Data
(optional)
236 bytes
Max: 240 bytes
Data Size:

## Slide 11: Building the MAC Frame
Data
(optional)
1-234 bytes
Frame Type
1 byte
Data Size
1 byte
Check Data
(optional)
1 byte
Receiver UE
1 byte
Sender UE
1 byte
We must be sure that the Data is transmitted without errors
CRC-8 to check the integrity of the bits
  simple and fast but does not correct errors.
Team 4 needs to be sure that the header is correct
Check
Header 1 byte
Max:240 bytes
Header: 5 bytes
CRC:

## Slide 12: Building the MAC Frame
ACK Frame:
Frame Type
1 byte
Data Size
1 byte
Receiver UE
1 byte
Sender UE
1 byte
Header Check
1 byte
5 bytes
Data
1-234 bytes
Frame Type
1 byte
Data Size
1 byte
Data Check
1 byte
Receiver UE
1 byte
Sender UE
1 byte
Header Check
1 byte
Max: 240 bytes
Header: 5 bytes
Data Frame:

## Slide 13: State Machine for Frame Transmission
Set Flag for Data Transmission
Create data frame
(Frame = header + data)
UE Sends & BS Receives
Read header
(Check Receiver ID in switching table)
Send to BS or UE?
BS Sends & BS Receives
BS Sends & UE Receives
Unpack frame
(Check the CRC of the header)
Check data CRC
Create ACK frame
Frame = header
Receiver = old Sender
Check data CRC
ACK
Data Corrupt
INVALID
CRC match
Drop frame
(Timeout will trigger)
Check Address Book for Receiver
Stop Timeout Counter
Timeout counter
Start
Stop
Timeout: Triggers re-send
UE
BS
DATA

## Slide 14: ACK Time Out
UE1
UE2
BS1
UE3
BS2
Shortest message
UE2 to UE1
UE1
UE2
BS1
UE3
BS2
To BS1
To UE1
To BS1
To UE2
To BS2
To UE1
Longest message
UE3 to UE1
UE1
UE2
BS1
UE3
BS2
UE1
UE2
BS1
UE3
BS2
UE1
UE2
BS1
UE3
BS2
Data
ACK
6 Time Slots
Data
To BS1
To BS2
ACK
12Time Slots
To BS1
To UE3

## Slide 15: Other Features Considered
Sequence number
  Sliding window
  Group ACK
NACK

## Slide 16: Implementation Constructor
Constructor Method
Verification of the number of inputs

## Slide 17: Implementation Constructor
Check for the minimum size
CRC check the header.
CRC check the header.
Failed checks result in INVALID frame types

## Slide 18: Implementation Data field
Maximum size of data field
Creation of CRC
Mapping chars to bits
Maximum size of data field

## Slide 19: Implementation Data field
Extract the data size
The dimensions of the input limit the data size
Maximum size of data field

## Slide 20: Implementation Receiving a Frame
Check The FrameType
Verify the data CRC
Drop Invalid Frame
Create only one ACK to send back

## Slide 21: Interfacing Diagram

## Slide 22: Interfacing with the Physical Modules
Teams 1, 2 & 3
  Format of the bits that are generated by FrameObj
    Length of the frame
    Order of the bits
  How to exchange data between the layers
    Flags to indicate new messages
    Callbacks
Team 3
  Additional processing to route the message

## Slide 23: Interfacing with the Network Modules
Team 4
  The ACK frame is reused
  The same basic frame construction is used
    Polling Frame
    Request Frame
Team 5
  The address table determines which physical resource will route the frames.
  The same basic frame construction is used
    Table Frame

## Slide 24: FrameType Functionality
Frame Type | Number Received
ACKFRAME | 2
DATAFRAME Correct CRC Corrupt CRC | 102 100 2
INVALID | 3466
Data Transmission with Transceiver from Lab 2
Frame Type | Number Received
ACKFRAME | 0
DATAFRAME Correct CRC Corrupt CRC | 165 161 4
INVALID | 3559
  False Detection of ACK frame because similar frameType numeric representation.
  We increased the hamming distance between the values of the types of frames to avoid false detection

## Slide 25: ‘End-to-End’ Simulation of Data Transmission and ACK Response Using Team 4’s Transceiver

## Slide 26: Lessons Learned
The Physical layer is very important, we cannot compensate for unreliable data transmission.
We can accommodate erroneous data through verifying the data range and considering possible received values
Hamming distance of the frame type are very important
More data types are needed for the control messages in the system than for transmitting data.